## Slide 1
Optimization and its need
Optimization is a program transformation technique, which tries to improve the code by making it consume less resources (i.e. CPU, Memory) and deliver high speed.
Compiler will apply optimization technics on code so that efficient code generated for execution

## Slide 2: Example:
Global variables modified by an interrupt service routine outside the scope:
For example, a global variable can represent a data port which will be updated dynamically. The code reading data port must be declared as volatile in order to fetch latest data available at the port. Failing to declare variable as volatile, the compiler will optimize the code in such a way that it will read the port only once and keeps using the same value in a temporary register to speed up the program (speed optimization). In general, an ISR used to update these data port when there is an interrupt due to availability of new data

## Slide 3: VOLATILE
The volatile keyword is intended to prevent the compiler from applying any optimizations on objects that can change in ways that cannot be determined by the compiler.
Objects declared as volatile are omitted from optimization because their values can be changed by code outside the scope of current code at any time. The system always reads the current value of a volatile object from the memory location rather than keeping its value in temporary register.